## Slide 1: Questions/avenues to be addressed by all of the instrument-related sessions throughout this day:
Questions/avenues to be addressed by all of the instrument-related sessions throughout this day:
How well can we define, observe, and measure those phenomena that are crucial to space- weather situational awareness and what do we really need going forward?
What are the barriers to delivery of the crucial observations/measurements?
What are the critical trade-offs between observations/measurements and cost?
How do we future-proof these data sets and link to improvements in modelling capabilities?

## Slide 2: advocating for identical magnetographs in l5 and l1
manolis k. georgoulis
RCAAM of the Academy of Athens
L5 in Tandem with L1
London, UK. 5 - 9 March, 2017

## Slide 3: what do we gain : VECTOR Magnetograph
  l5 in tandem with l1 manolis k. georgoulis
Assuming reliable obs. due to projection effects up to ±50o EW:
Start of reliable obs. ~6 days prior to crossing the L1 Western Limb
~1.5 days after crossing the L1 W limb, still reliable obs. from L5. Then, about ~1.5 days before reliable obs. are taken from L1

## Slide 4: what do we gain: LINE-OF-sight magnetograph
  l5 in tandem with l1 manolis k. georgoulis
Start of reliable obs. ~4 days prior to crossing the L1 Western Limb
Then, another ~4 days before reliable obs. are taken from L1. But a pretty good idea from L5, already
Assuming reliable obs. due to projection effects up to ±30o EW:

## Slide 5: magnetogram specifications
  l5 in tandem with l1 manolis k. georgoulis
Keeping in mind that this is an operational mission:
MDI-type magnetograph:
full-disk, 96-min cadence
~2” per pixel; 4” spatial resolution
HMI-type magnetograph:
full-disk, 12-min cadence
~0.5” per pixel; 1” spatial resolution
… or perhaps “HMI-type” spatial res. in an “MDI-type” cadence