## Slide 1: NOAA L1 Status and Studies
D.A. Biesecker1, D. Socker2
1NOAA/SWPC, 2DOD/NRL

## Slide 2: Outline
NOAA’s History at L1
  ACE
  DSCOVR
NOAA’s Future at L1
  SWFO
Coronagraph
  Requirements
  Requirements justification
  Cosmic Ray scrubbing
  Gap-filler

## Slide 3: NOAA’s L1 History (ACE & DSCOVR)
1993: NOAA Deputy AA provided funds for RTSW effort
1998: ACE became ‘operational’ for SWPC on 21 Jan 1998
2008: NOAA & USAF funded NASA to pull DSCOVR out of storage
2015: DSCOVR launched 11 Feb 2015
2016: DSCOVR became operational for SWPC 27 Jul 2016

## Slide 4: After DSCOVR comes SWFO
NOAA Space Weather Follow-on Program to follow DSCOVR at L1
Highlights of the planned mission are:
  Total 10 year operational mission
  Two identical spacecraft for long-term continuity
    Launches planned for 2022 and 2027
  Addition of a coronagraph – Compact Coronagraph (CCOR)
  Addition of a suprathermal ion sensor (e.g. ACE/EPAM) 10 keV - 2 MeV
  Improved plasma measurements for meeting more stringent user requirements – high plasma velocity (V=2500 km/s)

## Slide 5: Compact Coronagraph (CCOR)
NRL is in Phase A
  System Requirements Review/Concept Design Review held Feb 16, 2017
Phase B begins in April 2017

## Slide 6: L1 In-situ Requirements
L1 Requirements Workshop held in 2014
  In-situ and imaging sessions held in parallel
  Requirements (extended range) now cover extreme space weather
Parameter | Threshold | Objective
Magnetic Field Vector |  | 
Measurement Cadence | 1 vector per minute | 1 vector per second
Magnetic Field Range | 0 to ±200 nT along each axis | 
Accuracy | ±1 nT up to 100 nT 1% for measurement > 100 nT | 
Plasma Ion Velocity, Density, and Temperature |  | 
Measurement Cadence | 1 measurement per minute | 1 measurement per second
Velocity Range | 200 to 2500 km/s | 
Density Range | 0.1 to 150 particles per cm^3 | 
Temperature Range | 40,000 to 2,000,000 K | 
Low Energy Ion Particle Population |  | 
Measurement Cadence | 1 measurement every 5 minutes | 1 measurement per minute
Energy Range | 10 to 2,000 keV | 
Spectral Resolution | 5 differential flux channels per decade | 

## Slide 7: Coronagraph Requirements
Parameter | Threshold | Objective
Field of View | 3.7-17 RSUN | 3-25 RSUN
Pointing Knowledge | 25 arcsec | 12.5 arcsec
Knowledge of Solar North | 1 degree | 0.5 degree
Spatial Resolution | 50 arcsec (at average of the inner and outer radii of the FOV) | 
Photometric Accuracy | 10% | 
Image Cadence | 15 minutes | 5 minutes
Data Latency* | 15 minutes | 5 minutes
Field of view range
ΔFOV function of:
  # of CME images
  CME speed
  sampling frequency
  Assume fastest CME 3400 km/s
    (cf. LASCO catalog)
ΔFOV = (3*3400km/s*15min) =13.2 Rsun
*Data Latency is defined as the time from the end of the final exposure in an image, or image sequence, to the time the level 3 processed data are available to forecasters.

## Slide 8: CCOR will see through the ‘clouds’
CCOR
CME + SEP storm
COR2 CME
90% of pixels effected
Current state of the art (COR2)
CME+SEP STORM
90% of pixels effected
Using scrub algorithm
STEREO-A COR2 Image of CME (01/27/2012)

## Slide 9: Nominal CCOR Image Quality & Performance
75% Contamination
97% of all pixel samples contaminated
No Scrub
With Scrub
COR2 SEP free CME

## Slide 10: CCOR Scrub Algorithm
For Each Pixel, Go through the Stack of 30 and find the smallest value
Use the minimum pixel value to construct a tolerance for each pixel stack and search for other usable values
Using algorithm run time in C and a series of benchmark programs (whetstone, dhrystone) a 3 minute run-time for CCOR flight computer is estimated.
Notes: Histogram graph of values edit font size

## Slide 11: Gap-Filler Coronagraph
SOHO is nearing the end of it’s lifetime
  1000 Watts needed to recover from safe mode
SWFO launch planned for 2022
  Risk of no coronagraph data
NOAA exploring options for a CCOR tech demo deployment ~2019
  e.g. RFI released in 2016

## Slide 12: Summary
Space Weather Follow On, with the first launch in 2022, represents NOAA’s intent to provide continuous monitoring of solar wind data from L1
  It also represents the first operational coronagraph
Mission definition for SWFO is at a very preliminary stage
Loss of SOHO before SWFO is operational is a real risk that NOAA is taking seriously