## Slide 1: SWAVES-like radio instrument?
STFC RAL Space (UK)
Mario M. Bisi
Royal Observatory of Belgium
Jasmina Magdalenić
Notes: This is the adapted figure from the STEREO WAVES page.

## Slide 2: SWAES like radio instrument in L5 and L1?
What products/data we what to obtain?
Solar radio observations: Dynamic radio spectra & Direction finding observations
Adapted from: http://secchirh.obspm.fr/
Dynamic radio spectra by STEREO/WAVES & WIND/WAVES showing type II and type III bursts on 2014 January 07.
Type II bursts:
1D shock wave speed  gives indication on the CME speed.
Prediction of the shock arrival at 1 AU (Cremades et al., 2007, 2015).
Type III bursts:
Indication on the open field lines.
Notes: Here I have mentioned only the straight forward use of type II bursts, it is a bit hard to list down all the options – like the one I have mentioned on my talk at Jeju…
The reference of Cremades et all, is because she demonstrated how the prediction of the shock arrival at 1 AU using interplanetary type II radio bursts is actually quite good. I like the first article better.

## Slide 3: Solar radio observations: Dynamic radio spectra & Direction finding observations
Adapted from: Magdalenić et al., 2014
Radio measurements of STEREO/WAVES showing type II burst on 2012 March 05.
Radio flux density, Colatitude of wave vector and Azimuth of wave vector.
Signal to noise ration for SWAVES A observations is too low to obtain reliable results or radio triangulation.
Type II bursts – 3-D shock wave speed and position in space of the radio-loud part of the shock wave.
Type III bursts – indication on the open field lines.
Notes: I did not list the relevant publications, it would overcrowd the presentations, and it does not seem so important to me.

## Slide 4: Instrument specifications 1:
Physical range:
Solar radio spectra from 10 kHz to 60 MHz.
Split into a few sub-bands, i.e. a few receivers.
The high frequency part (10 − 60 MHz range), should be used for inter-calibration with ground-based observations.
Time range & Latency:
Continuous coverage.
Updated every 10 – 40 min.
Can we go up to 60 MHz?
WAVES-like instruments typically go up to about 20 MHz only.
Dynamic range:
Depends on the frequency range.
< 150 kHz, 110 dB.
> 150 kHz, 80 dB.
> 30 MHz, 50 dB.
All the specification are concerning the SWAVES-like radio instruments.

## Slide 5: Instrument specifications 2:
Time resolution:
Depends on the frequency range.
< 150 kHz; 10 s // 20 s // 30 s
> 150 kHz; 1 s // 3 s // 5 s
> 30 MHz; 0.1 s// 0.2 s // 0.4 s
Frequency resolution:
Depends on the frequency range.
< 125 kHz; ∆f/f =9%
125 kHz – 15 MHz; 100 kHz
> 15 MHz; 10 kHz
Interplanetary type II bursts have patchy structure and substructures lasting less then 1 min and having bandwidth of less than 0.1 MHz (for frequencies ≤ 1 MHz where direction finding observations are usually considered).
Resolution of 1 min is not sufficient, in particular for direction finding observations!
All the specification are concerning a SWAVES-like radio instrument.
Direction finding below 400 kHz with SWAVES instruments gives somewhat unreliable results (Krupar et al., 2014, Magdalenić et al., 2014).
Notes: The brown values are wanted, then// medium level, then // threshold level.

## Slide 6: Waves like radio instrument in both L5 and L1.
Why the same instrument for both missions?
For the space weather forecasting purposes:
Intensity of the radio emission, as seen from two different spacecraft is directly comparable  straightforward idea on the direction of the propagation of the CME-driven shock and CME itself (using only dynamic spectra).
Better, i.e. more exact, results of the radio triangulation (errors are usually considerably large for a single instrument).
Easier to cross-calibrate two identical instruments.
Some recent evidence has shown that the near-Sun detections of shocks (at higher frequencies) have provided a better proxy for CME speed (since the shock and CME front are still travelling at approximately the same speed close-in to the Sun) and with two simultaneous detections, a measure of the direction can also be given.
On the space-weather science side, there is evidence that some Type II emission doesn’t come from the nose of the CME/shock, but from the flanks, and this needs further investigations.