## Slide 1
WG1 - Visible light imaging of the corona & heliosphere
Russell A Howard (NRL)
Richard A Harrison (RAL)
with
Angelos Vourlidas (APL/JHU)
Jackie A Davies (RAL)

## Slide 2
WG1 – Visible light imaging of the corona/heliosphere
Last workshop – WG1 set up to consider/debate coronagraph and heliospheric imager space weather strategy
However, L1/L5 SW mission studies have been pursued on either side of the Atlantic – most appropriate added value here is to compare and debate, in particular the differences between the European and US conclusions
Studies/activities:
  Two ESA L1/L5 studies (2015-16)
  US DSCOVR follow-on mission
  UK Carrington mission study
  Helio Decadal White Papers (research payload)
  UK IPSP project
  Others

## Slide 3
All studies call for a coronagraph as a core element of the mission payload to identify the launch of CMEs providing speed and mass
A heliospheric imager is seen as key to most L5 concepts, as well as some L1 concepts to confirm the CME measurements, formation of CIRs & CME Bfield.
Broad agreement, but some differences
The rest of the presentation:
  US perspective/conclusions
  European perspective/conclusions
  Questions/debate relating to a comparison of the two and of outstanding issues
WG1 – Visible light imaging of the corona/heliosphere

## Slide 4
L1: SWFO is on the way to becoming a real mission
  CCOR is in Phase A development, SRR held last month, Phase B next month
  SWPC believes WL Coronagraph absolutely necessary – HI does not improve accuracy-therefore not necessary
L5: No official (NOAA or NASA) direction
  Research option: L5 highly rated in Helio Decadal for mid-2020s Unconnected to a mission line.
    Orbit about L5 providing a range of heliographic longitudes
  Operational option: No NOAA requirements (or definition efforts) Possible operational reqs:
      COR 2.5 – 20 Rs (models initialized at 20 Rs)
      Should it be a copy of L1 COR?
      HI optional, <40˚, ~0.7AU (up to 1 day prediction is sufficient)
    Possible R2O reqs:
      EUV COR ( <2.5) + HI (< 40˚)
      Polarization capability?
WG1 – Coronagraphs & Heliospheric Imagers: USA

## Slide 5: NOAA CME Imager Requirements-1
Item | Requirement
Field of View | 3.7Rsun – ≥ 17Rsun (3-25 Rsun goal)
Spatial Resolution | 50 arc-secs @ mid FOV (10.35 Rsun)
Spectral Response | “White Light”; 500nm ≤ bandpass ≤ 800nm
Spatial Response Uniformity | ≤ 5% over FOV
Flux Resolution | ≤ 1x10-12 in the outer FOV. ≤ 5x10-11 (Goal 1x10-11) inner FOV. Units: B/Bsun/pixel
Measurement Range | Min ≤ 1x10-11; Max ≥ 1x10-8 (Goal: 5x10-8); Straylight ≤ 5 x10-12 (Goal: 1x10-12). Units: B/Bsun; Measured at FOV (10.35 Rsun).
Absolute Accuracy | Calibrated to an absolute accuracy of 25%. Goal 10%.
Defective Pixels | Single exposure raw data image ≤ 0.1%.
Inflight Calibration | Commandable illumination source. Constant, relative, flat fielding, photometric standard throughout instrument life.

## Slide 6: NOAA CME Imager Requirements-2
Item | Requirement
Data Cadence | One full-FOV image at least every 15 min. Exposure time of < 15 seconds, (Goal: 7.5 seconds).
Data Latency | Time from the completion of image integration to the transmission of the last image bit to the spacecraft data bus, shall be no more than 2 minutes (Goal: <30 s). Shall not exceed 15 minutes (delivery to NOAA/SWPC).
Partial Image Readout | Provide partial images of the FOV via partial detector readout. Configurable.
Data Compression | Uncompressed; Lossless (1); lossy (1)
Binning and Summing of Pixels | 1x1; 2x2 binning.

## Slide 7: CCOR Concept Origins
CCOR
STEREO/SECCHI/COR2
STEREO/SECCHI/HI
Apply HI-1 (WISPR & SoloHI) design solution
after first lens
Apply COR2 design solution
up to first lens
STEREO/SECCHI
COR2
first lens
HI-1
HI-2

## Slide 8
WG1 – Coronagraphs & Heliospheric Imagers: Europe
ESA L1/L5 Studies: Objectives (relevant to coronagraph and heliospheric imager)
(L1) To identify the launch of Earth directed CMEs, and their motion away from the Sun, including the prediction of arrival times at Earth.
(L1 & L5) To provide improved inputs to heliospheric models, including estimates of the background solar wind and CME parametrisation, to improve CME arrival time and solar wind predictions at Earth.
(L5) To provide improved assessment of CME motion and density, in the corona and heliosphere, using a different observational perspective to the L1 observations.
Note: We take ESA SSA L1/L5 studies as representative

## Slide 9
ESA L1/L5 Studies: Payload
L1 Coronagraph (critical), Heliospheric Imager (optimal)
L5 Coronagraph (critical), Heliospheric Imager (critical)
Strawman instruments (next slides) incorporate ‘Threshold’ and ‘Goal’ options (slides courtesy of Stefan Kraft, ESA)
WG1 – Coronagraphs & Heliospheric Imagers: Europe

## Slide 10: (5) Coronagraph
Measurement objective
  Definitive, early and critical identification of Earth‐directed CMEs
  Forecasting, with the longest possible lead time, of CME arrival at Earth
  Characterisation of CMEs for inclusion into the majority of current operational modelling endeavours to predict their Earth arrival
Performance requirements
 FoV: 3 ‐ 22 Rs (2.5 ‐ 30 Rs)
  Spatial resolution: 2 arcmin
  Dynamic range: 16 bits (ADC)
  Accuracy: 20% of CME signal
  Sensitivity: detection of signal to 2 x 10‐13 Bo
 SNR > 2 (>4)
  Cadence: 10 min (5 min)
  Latency:
L1: 15 min (5 min) L5: 25 min (15 min)
Note Jackie’s presentation….

## Slide 11
(5) Coronagraph
Heritage
  LASCO C2 & C3 and COR2
  Through occultation of the solar disc provide imagery of the near‐Sun K‐ corona and CMEs or CME shocks therein
  Detect broad‐band visible light via Thomson scattering of sunlight from electrons.
Instrument baseline
  Solar Coronagraph for OPErations (SCOPE)
ESA GSTP development
Developments
  Current development limited to BB
  EQM development needed to reach TRL 6 by 2019
Size: Sensor unit: 600x250x
250 mm3
DHU: 230x200x
80 mm3
Mass: 18 kg
Power: 25 W Telemetry:
~10 kbps
See Middleton et al, ICSO paper 55

## Slide 12: (8) Heliospheric Imager
Measurement objective
  Tracking (imaging) of Earth‐directed CMEs and shocks over much of their propagation path
  Mitigate deficiencies in arrival times predictions based on the use alone of near‐Sun data
  Provide information on the background solar wind
Performance requirements
  FoV: L1: 10 to 40 deg, L5: 4 to 60 deg (10 to 60 deg)
  Spatial resolution: 4 arcmin
  Dynamic range: ~1x10‐11 to ~3x10‐13 of B0 (G‐FoV)
  Detection of intensity down to ~ 10‐14 Bo (3x 10‐15 Bo)
  Cadence: 60 min (30 min)
 Latency: L1: 20 (10) min, L5: 25 (15) min
  Accuracy: 20% of CME signal

## Slide 13: (8) Heliospheric Imager
Heritage: STEREO HI (2 CCD based cameras)
Measurement principle
  Imaging of the solar wind broad‐band visible sun light (Thomson scattering on electrons)
  Low signal, high dynamic range (24 bit after multiple image acquisition)
L1 configuration
  Two instruments each one camera
  Angular range from 10 to 40 deg  goal: 4 to 60 deg
L5 configuration
  2 cameras within one instrument
  Cover complete range between Sun and Earth (4 to 60 deg) or beyond
Development for Lagrange missions
  FoV optimisation and resource reduction
  Harmonisation of L1 and L5 configuration
  Use state of the art technologies
(baffling, coating, detector electronics)
Exploitation of polarisation properties of the scattered light (optional)
Space Weather. 2016 Jan; 14(1): 32–49.

## Slide 14
WG1 – Coronagraphs & Heliospheric Imagers
DISCUSSION & DEBATE

## Slide 15
WG1 – Coronagraphs & Heliospheric Imagers
Particular areas for debate:
Coronagraph
  FOV ESA SSA -Threshold 3-22 Rs; Goal 2.5-30 Rs US <20 Rs?
  Cadence ESA SSA T(G) 10 (5 min) US 15 min
  Latency ESA SSA L5 T(G) 25 (15) min US 15 min
  ESA SSA L1 T(G) 15 (5) min US 15 min
  On board processing challenges
Heliospheric Imager
  Should there be HI at L1? Do we agree on L5?
  FOV - ESA-SSA - 4-60 degrees; US - <40 degrees?
  Cadence & Latency
  On board processing challenges
  Polarisation capability?
  “Mitigation of potential pitfalls of only being reliant on near Sun data” (mid course corrections; CME-CME interaction; accel/decel)

## Slide 16
WG1 – Coronagraphs & Heliospheric Imagers
Other areas for debate:
Requirements
  Do the ESA SSA L1/L5 study requirements fit the bill? (Deliverable of the project – not defined by ESA)
  Why no US requirements for L5?
Science Research
  To what extent do we/should we press for science research projects to develop the field/knowledge base/capability?
  Have we ‘oversold’ the space weather story to support science missions?

## Slide 17
WG1 – Coronagraphs & Heliospheric Imagers
Other areas for debate:
Can we simply adapt science instruments for operational use?
  In principle, yes (for these two instruments), but, no bells and whistles?
Any major technological bars to taking instruments in flight and adapting for operational use?
  STEREO COR2 and HI would be good, but 15 year old technology
  SOHO LASCO – flexible 3-part coronagraph system – 25 year old technology
  Solar Orbiter METIS includes flexibility of a science mission;
  Solar Orbiter/SoloHI and Solar Probe Plus/WISPR?

## Slide 18
WG1 – Coronagraphs & Heliospheric Imagers
Other areas for debate:
What advances are required to exploit coronagraph and heliospheric imaging data more effectively, in the near and further future, for space weather application?
    Models, data analysis/processing
What is the roadmap for demonstrating new developments, such as polarized heliospheric imaging, that are potentially beneficial for space weather operations? …or are they?

## Slide 20
WG1 – Coronagraphs & Heliospheric Imagers
Instrument | FOV | Comment
LASCO/C2 | 2.2 - 6 Rs | 
LASCO/C3 | 3.7 – 30 Rs | 
STEREO/COR2 | 2.5 – 15 Rs | 
Solar Orbiter/METIS | 5.5 – 11 Rs | 1 AU equivalent. Variable Sun-S/C distance. FOV is 1.5 to 2.9 degrees
STEREO/HI | 4 - 24 deg & 18 - 88 deg | 
SoloHI | 5.5 – 45 deg | 1 AU equivalent. 40 deg FOV, 5 deg from Sun-centre
WISPR | 13.5 – 104 deg | 1 AU equivalent.